CHAPTER 2
CHAPTER 2
Data Transmission media

---
Data Transmission Media
Data Transmission Media
- Data Transmission: The process of conveying data between two points by way of a communication medium.
- A wide variety of media are available, but they fall into two classes;
  - Bounded media: Confine the data to specific physical pathways.
    - Common examples include copper wire and optical fiber cables.
  - Unbounded media: Transmit the data-carrying signal through space, independent of a cable.
    - Broadcast radio and television are examples of unbounded media.

---
Two Important Physical Limits of a Transmission System
Two Important Physical Limits of a Transmission System
- Propagation delay
  - Time required for signal to travel across media
  - Example: electromagnetic radiation travels through space at the speed of light (c = 3108 meters per second)
- Bandwidth
  - Maximum times per second the signal can change

---
Characteristics to be considered when examining cables
Characteristics to be considered when examining cables
- Electrical magnetic interference (EMI):
  - Many electrical devices generate magnetic fields that produce unwanted electrical currents in data cables.
  - Common sources of EMI include Electrical motors, fluorescent lights etc.
- Bandwidth: The range of frequencies that the cable can accommodate.
- Attenuation: Signal strength reduces with distance.
  - Electrical resistance contributes to this.
- Cost: Depends on choice of cable

---
Forms of energy used to transmit data
Forms of energy used to transmit data
- Audible sounds
- Electric current
- Light
- Omni-directional electromagnetic waves
  - Radio Frequency (RF)
  - Infrared
- Directional electromagnetic waves
  - Point-to-point satellite channel
  - Limited broadcast (spot beam)
  - Microwave
  - Laser beam

---
Transmission Media
Transmission Media
- The transmission capacity depends on the distance and on whether the medium is point-to-point or multipoint
- Two major classes
  - Conducted/Guided/Bounded media
    - Use a conductor such as a wire or a fiber optic cable to move the signal from sender to receiver.
  - Wireless/Unguided/Unbounded media
    - Use radio waves of different frequencies and do not need a wire or cable conductor to transmit signals.

---
Transmission Media

---
Twisted Pair Wires
Twisted Pair Wires
- Consists of two insulated copper wires arranged in a regular spiral pattern to minimize the EMI between adjacent pairs
- Often used at customer facilities and also over distances to carry voice as well as data communications
- Low frequency transmission medium

---
Twisted Pair Wires
- Two varieties
  - STP (shielded twisted pair)
    - the pair is wrapped with metallic foil or braid to insulate the pair from electromagnetic interference
  - UTP (unshielded twisted pair)
    - Each wire is insulated with plastic wrap, but the pair is encased in an outer covering

---
Twisted Pair
Twisted Pair
- UTP cables come in a variety of grades, ranging from Cat 1(lowest quality) to Cat 7 (highest quality).
  - When investigating the use of UTP cabling, determine the wire quality required for the network.

---
Twisted Pair Strengths and Weaknesses
Twisted Pair Strengths and Weaknesses
- Strengths
  - Inexpensive and readily available
  - Flexible and light weight
  - Easy to work with and install
- Weaknesses
  - Susceptibility to EMI and noise
  - Attenuation problem
  - Relatively low bandwidth (3000Hz)
  - STP is even more expensive, harder to work with

---
Coaxial Cable (or Coax)
Coaxial Cable (or Coax)
- Bandwidth of up to 400 MHz
- Has an inner conductor surrounded by a braided mesh
- Both conductors share a common center axial, hence the term “co-axial”

---
Coaxial Cables
Coaxial Cables
Coax cable is terminated using the BNC (Bayonet Neill-Concelman) connectors

---
Coaxial Cables
- The coaxial cable transmission media is used in two transmission methods
- Baseband
  - This has the following characteristics
    - It transmits unmodulated digital signals
    - Each cable carries a single channel
    - The propagation of signals is bi-directional
    - Stations are connected via T-connectors.
    - There is no need for modems.

---
Coaxial cable
Coaxial cable
- Broadband
  - It has the following characteristics
    - Digital signal modulated onto Radio Frequency (RF) carrier (analog)
    - Channel allocation based on Frequency Division Multiplexing (FDM).
    - Supports bi-directional transmission
    - Stations are connected via RF modems.

---
Coax Strengths and Weaknesses
Coax Strengths and Weaknesses
- Strength
  - Higher bandwidth
    - 400 to 600Mhz
    - Up to 10,800 voice conversations
  - Can be easily tapped (pros and cons)
- Weaknesses
  - Much less susceptible to interference than twisted pair
  - High attenuation rate makes it expensive over long distance
  - Bulky

---
Fiber Optic Cable
Fiber Optic Cable
- Glass or plastic transmission medium
  - used by telephone companies in place of long-distance trunk lines
  - Also used in implementing local data communications networks
- Consists of three concentric sections

---
Optical Fibers
Optical Fibers
- The parts of the cable are as follows:
  - The Light Conductor: A very fine fiber core.
    - Glass is the most common material, allowing signals to be transmitted for several kilometers without being refreshed.
    - Plastic is used in some circumstances, but plastic cables allow only short cable runs.
  - The Cladding: A glass layer that surrounds the optical fiber core. (lower refractive index than the light conductor
    - The optical characteristics of the cladding reflect light back to the core, ensuring that little of the light signal is lost.
  - An outer Jacket: Protects the cable from damage.
    - A single jacket can be used to bundle multiple core/cladding fibers into a multi-fiber cable.

---
Optical Fibers
- The light signals on fiber optic cables are generated either by
  - light emitting diodes (LEDs) or by injection laser diodes (ILDs),
- ILDs are similar to LEDs but produce laser light.
  - The purity of laser light is desirable, increasing both data rates and transmission distance.
- Light emitting diode (LED) or laser injects light into fiber. The light rays in the glass are totally reflected inside the core of FO has to have higher refractive index than cladding and also angle of incidence of light ray is greater than critical angle for core and its cladding.
- Signals are received by Photodiodes, solid state devices that detect variations in light intensity.

---
Fiber Optic Types
Fiber Optic Types
- Multimode step-index fiber
  - The reflective walls of the fiber move the light pulses to the receiver.
  - Common MM core sizes are 50 µm and 62.5 µm.
- Multimode graded-index fiber
  - Acts to refract the light toward the center of the fiber by variations in the density
- Single mode fiber
  - The light is guided down the center of an extremely narrow core.
  - The core size is typically 8.3 µm.

---
Fiber Optic Signals
Fiber Optic Signals
fiber optic multimode
step-index
fiber optic multimode
graded-index
fiber optic single mode

---
Fiber Optic Signals

---
Types of Optical Fibers
Types of Optical Fibers

---
Basic Optical Fibre Communication System
Basic Optical Fibre Communication System
An Optical Fiber Communication System consists of
- Transmitter
  - Optical source (LED or Laser diode) + driver circuit
- Optical Fibre
  - Single mode fibre, or
  - Multimode fibre
- Receiver
  - Photodetector PIN or APD + receiver circuit

---
Basic Optical Fibre Communication System

---
Basic Optical Fibre Communication System

---
Fiber Optic Advantages
Fiber Optic Advantages
- Greater capacity (bandwidth of up to 2 Gbps)
- Smaller size and lighter weight
- Lower attenuation(fewer repeaters due to low attenuation of fibers)
- Immunity to environmental interference
- Highly secure due to tap difficulty and lack of signal radiation
- Long lengths; Long, continuous lengths also provide advantages for installers and end-users.

---
Fiber Optic Disadvantages
Fiber Optic Disadvantages
- Expensive over short distance
- Requires highly skilled installers
- Adding additional nodes is relatively difficult
- Special devices are required to convert light signals into data or voice and vice versa.

---
Wireless (Unguided Media) Transmission
Wireless (Unguided Media) Transmission
- Transmission and reception are achieved by means of an antenna
- Directional
  - Transmitting antenna produce a focused beam
  - Transmitter and receiver must be aligned
- Omni directional
  - Signal spreads out in all directions
  - Can be received by many antennas

---
Radio wave propagation Modes
Radio wave propagation Modes
- Ground-wave propagation
- Sky-wave propagation
- Line-of-sight propagation

---
Ground Wave Propagation
Ground Wave Propagation
- Follows contour of the earth
- Can Propagate considerable distances
- Frequencies up to 2 MHz
- Example; AM radio

---
Sky Wave Propagation
Sky Wave Propagation
- Signal reflected from ionized layer of atmosphere back down to earth
- Signal can travel a number of hops, back and forth between ionosphere and earth’s surface
- Reflection effect is caused by refraction

---
Line-of-Sight Propagation
Line-of-Sight Propagation
- Transmitting and receiving antennas must be within line of sight
  - Satellite communication – signal above 30 MHz not reflected by ionosphere
  - Ground communication – antennas within effective line of site due to refraction
- Refraction – bending of microwaves by the atmosphere
  - Velocity of electromagnetic wave is a function of the density of the medium

---
Impairments and Capacity
Impairments and Capacity
- Impairments exist in all forms of data transmission
- Analog signal impairments result in random modifications that impair signal quality
- Digital signal impairments result in bit errors (1s and 0s transposed)

---
Transmission Impairments
Transmission Impairments
- Attenuation
  - loss of signal strength over distance
- Phase Distortion
  - Clipping or change in shape of waveform of a signal
- Delay Distortion
  - Signals arrive at receiver at different times due to different speeds for different frequencies
- Noise- signal that tends to interfere with desired signal
[Speaker Notes: 6]

---
Degradation of signals
Degradation of signals

---
LOS Wireless Transmission Impairments
LOS Wireless Transmission Impairments
- Attenuation and attenuation distortion
- Free space loss
- Atmospheric absorption
- Multipath
- Refraction
- Noise

---
Attenuation
Attenuation
- Strength of signal falls off with distance over transmission medium
- Attenuation factors for unguided media:
  - Received signal must have sufficient strength so that circuitry in the receiver can interpret the signal
  - Signal must maintain a level sufficiently higher than noise to be received without error
  - Attenuation is greater at higher frequencies, causing distortion

---
Categories of Noise
Categories of Noise
1. Thermal Noise 2. Intermodulation noise 3. Crosstalk 4. Impulse Noise
Thermal Noise/ white noise
- Thermal noise is due to agitation of electrons
- Present in all electronic devices and transmission media
- Cannot be eliminated
- Function of temperature
- Particularly significant for satellite communication

---
Categories of Noise
- Intermodulation noise – occurs if signals with different frequencies share the same medium
  - Interference caused by a signal produced at a frequency that is the sum or difference of original frequencies
- Crosstalk – unwanted coupling between signal paths, very common in twisted pair cables.
- Impulse noise – irregular pulses or noise spikes
  - Short duration and of relatively high amplitude
  - Caused by external electromagnetic disturbances, or faults and flaws in the communications system

---
Other Impairments
Other Impairments
- Atmospheric absorption – water vapor and oxygen contribute to attenuation
- Multipath – obstacles reflect signals so that multiple copies with varying delays are received
- Refraction – bending of radio waves as they propagate through the atmosphere

---
Error Compensation Mechanisms
Error Compensation Mechanisms
1. Forward error correction
Transmitter adds error-correcting code to data block
  - Code is a function of the data bits
Receiver calculates error-correcting code from incoming data bits
  - If calculated code matches incoming code, no error occurred
  - If error-correcting codes don’t match, receiver attempts to determine bits in error and correct
2. Adaptive equalization
Can be applied to transmissions that carry analog or digital information
  - Analog voice or video
  - Digital data, digitized voice or video
- Used to combat inter-symbol interference
- Involves gathering dispersed symbol energy back into its original time interval

---
Error Compensation Mechanisms
3. Diversity techniques
- Diversity is based on the fact that individual channels experience independent fading events
- Space diversity – techniques involving physical transmission path
- Frequency diversity – techniques where the signal is spread out over a larger frequency bandwidth or carried on multiple frequency carriers
- Time diversity – techniques aimed at spreading the data out over time

---
Wireless Examples
Wireless Examples
- Terrestrial microwave transmission
- Satellite transmission
- Broadcast radio
- Infrared

---
Terrestrial Microwave Transmission
Terrestrial Microwave Transmission
- Uses the radio frequency spectrum, commonly from 2 to 40 Ghz
- Transmitter is a parabolic dish, mounted as high as possible
- Used by common carriers as well as by private networks
- Requires unobstructed line-of-sight between source and receiver
- Curvature of the earth requires stations (called repeaters) to be ~30 miles apart

---
Microwave Transmission Applications
Microwave Transmission Applications
- Long-haul telecommunications service for both voice and television transmission
- Short point-to-point links between buildings for closed-circuit TV or a data link between LANs

---
Microwave Transmission Strengths and Weaknesses
Microwave Transmission Strengths and Weaknesses
- Advantages
  - No cabling needed between sites
  - Wide bandwidth
  - Multi-channel transmissions
- Disadvantages
  - Line-of-sight requirement
  - Expensive towers and repeaters
  - Subject to interference such as passing airplanes and rain

---
Satellite Microwave Transmission
Satellite Microwave Transmission
- A microwave relay station in space
- Can relay signals over long distances
- Geostationary satellites
  - Remain above the equator at a height of 22,300 miles (geosynchronous orbit)
  - Travel around the earth in exactly the time the earth takes to rotate

---
Satellite Transmission Links
Satellite Transmission Links
- Earth stations communicate by sending signals to the satellite on an uplink
- The satellite then repeats those signals on a downlink
- The broadcast nature of the downlink makes it attractive for services such as the distribution of television programming

---
Satellite Transmission Process
Satellite Transmission Process

---
Satellite Transmission Applications
Satellite Transmission Applications
- Television distribution
  - A network provides programming from a central location
  - Direct broadcast satellite (DBS)
- Long-distance telephone transmission
  - High-usage international trunks
- Private business networks

---
Principal Satellite Transmission Bands
Principal Satellite Transmission Bands
- C band: 4(downlink) - 6(uplink) GHz
  - the first to be designated uses large dishes
- Ku band: 12(downlink) -14(uplink) GHz
  - Uses smaller dishes. Rain interference is the major problem
- Ka band: 19(downlink) - 29(uplink) GHz
  - equipment needed to use the band is still very expensive

---
Satellite Advantages and Disadvantages
Satellite Advantages and Disadvantages
- Advantages
  - Can reach a large geographical area
  - High bandwidth
  - Cheaper over long distances
- Disadvantages
  - High initial cost
  - Susceptible to noise and interference
  - Propagation delay

---
Common Carriers
Common Carriers
- A government-regulated private company
- Involved in the sale of infrastructure services in transportation and communications
- Required to serve all clients indiscriminately
- Services and prices from common carriers are described in tariffs

---
The Electromagnetic Spectrum
The Electromagnetic Spectrum
Long radio waves
Microwaves
X-rays
Gamma rays
TV, FM
Infrared
Ultraviolet
700 nm
600 nm
500 nm
400 nm
4.5x1014 Hz
5x1014 Hz
6x1014 Hz
7x1014 Hz

---
Electromagnetic Spectrum for Transmission Medium
Electromagnetic Spectrum for Transmission Medium